## Slide 1
Ghost-Lattice x Your Arm
Move the hand with a thought. Stop it with a jaw clench.
Eric (Elbàlor / The Digital Necromancer) - demo walkthrough for Arinzay - October 2026
Ghost-Lattice QNN - backprop-free quantum reservoir computing

## Slide 2
Our two jobs
Eric - the software side:
The laptop runs the Ghost-Lattice 'brain': it reads the headband, decides OPEN / CLOSE / REST, and sends one letter to the arm.
The brain was trained ONCE, long before today. It never changes at demos.
Arinzay - the hardware side:
Wear the headband. Follow the 2-minute calibration prompts.
The arm: flashed firmware, servo + relay + panic button wired, 'GL-ARM ready' on screen.
You never touch the math. You wear the sensor; the arm obeys.

## Slide 3
What happens when you think 'close'
1. Headband picks up your EEG (22 channels, streamed over LSL).
2. The Rheon gate smooths the raw signal in time - same idea as the iris of an eye adapting, but it is a tiny learned filter.
3. A frozen 29-qubit quantum-style reservoir + feature forge turns the smooth signal into ~33,000 numbers.
4. YOUR 2-minute calibration readout translates those numbers into one word: OPEN, CLOSE, or REST.
5. Five votes in a row (~1.25 s) before the command is sent - no twitch on single spikes.
6. One letter goes down the USB cable. The arm glides.
Total loop: a quarter of a second. The quantum part is frozen; only step 4 is about you.

## Slide 4
Calibration: 2 minutes, once per person
There is NO training session. The brain is already trained. This is a fitting, not a lesson:
1. REST - relax, think of nothing (20 s)
2. CLOSE - imagine slowly closing your hand (20 s)
3. OPEN - imagine slowly opening your hand (20 s)
4. JAW CLENCH - clench as hard as you can (10 s) -> this sets your personal emergency-stop threshold
The computer solves one convex equation with a closed-form answer. No waiting, no 'epoch 47 of 500'. Your profile is saved (profiles/arinzay.npz) - next time you skip straight to live.
Different person = different profile file. The frozen brain never changes.

## Slide 5
The whole contract: four letters
Laptop sends The arm does
O glide to OPEN (critically damped, zero jitter)
C glide to CLOSE
R glide to REST (neutral)
S DISTRESS STOP - relay cuts servo power, LATCHED
A re-arm power - operator-only, never automatic
The arm boots UNPOWERED. Power exists only after an explicit 'A'.
Motion is smoothed inside the firmware itself (critically damped ODE) - even a command burst cannot make the hand jitter.
Protocol: 115200 baud USB serial - firmware: firmware/prosthetic_arm/prosthetic_arm.ino

## Slide 6
Safety: two independent kill switches
1. Jaw-clench distress stop (software, parallel to everything):
Clenching fires a fixed-threshold detector on 20-60 Hz EMG - fixed threshold, deliberately NOT learned, calibrated on YOUR clench in step 4 of setup.
It sits BESIDE the decode pipeline, never after it. If the laptop hangs, the relay still answers the last 'S'.
2. The panic button (pure hardware):
A physical button wired straight to the Arduino cuts servo power even if every laptop, cable and line of code dies mid-demo.
Plus the boot rule: the arm always starts UNPOWERED, and power returns only when the operator sends 'A'.
Rule from the paper: nothing learned ever stands between a person and a moving motor.

## Slide 7
Arinzay's 10-minute wiring checklist
1. Servo: brown = GND, red = battery 5 V, orange (signal) = D9.
2. Relay module: VCC = 5 V, GND = GND, IN = D7. The servo's red wire goes THROUGH the relay's NO contact: battery + -> relay -> servo.
NEVER feed the servo from the Arduino's 5 V pin - that is what causes jitter. Power through the relay/battery.
3. Panic button: one leg to D2, other leg to GND (the firmware uses INPUT_PULLUP; pressed = LOW).
4. Laptop USB -> Arduino. That cable is the entire link.
5. Range-test the panic button before every audience.
Flash prosthetic_arm.ino, power on, expect: 'GL-ARM ready (power OFF; send A to arm)'

## Slide 8
Running a session (Eric's side)
python run_live_bci.py --simulate rehearsal - fake headband, no hardware
python run_live_bci.py --simulate --port COM5 bench test - rehearsal brain, real arm
python run_live_bci.py --lsl --port COM5 --profile profiles/arinzay.npz the real thing
First run for a new user launches the calibration wizard automatically; later runs load the saved profile.
Ctrl+C ends the session - and the script always sends 'S' (stop) on exit, whatever happens.
Simulate first. Always. The real headband only after the rehearsal is boring.

## Slide 9
The demo, minute by minute
0:00 Arm bench-tested (O / C / R from the keyboard), relay click audible on 'S'. Panic button range-tested.
2:00 Arinzay wears the headband. Calibration wizard: REST, CLOSE, OPEN, JAW CLENCH - two minutes, four prompts.
4:00 Operator sends 'A' - the arm powers for the first time.
4:30 Arinzay thinks 'close' - the hand closes. Thinks 'open' - it opens. She is moving a machine with her brain.
6:00 Dramatic finish: she clenches her jaw - the relay CLICKS and the arm goes dead. Safety is the show.
The ask: 'nothing learned stands between me and the motor' - say it out loud, it is the whole point.
If the crowd asks how it works: one frozen brain, one 2-minute fit, two kill switches.

## Slide 10
If something misbehaves
Symptom -> Likely cause -> Fix
No LSL stream found -> headband app not streaming -> start its LSL outlet, run --lsl again
Works in rehearsal, wrong live -> cap shift / refit -> recalibrate (2 min) - the readout handles her
Arm jitters -> servo powered from Arduino 5V -> power through the relay/battery
E-stop fires in normal use -> clench threshold too low -> recalibrate with a harder clench
Five-minute self-test any time: from ghost_lattice.safety import selftest; print(selftest())

## Slide 11
Five words, so you can answer anyone
Rheon gate
- the tiny filter that smooths your brain signal in time before anything else touches it.
Quantum reservoir
- a frozen 29-qubit physics simulation that turns smooth signal into ~33,000 numbers. Never retrained.
Readout / calibration
- the only part that knows YOU: one convex equation solved in closed form from your 2 minutes.
Zeta smoothing
- the hand moves like it has gentle mass and damping - glides, never snaps.
Distress stop
- your jaw clench, a fixed threshold, and a relay that cuts the power. Always wins.
Paper: Ghost-Lattice_QNN_Paper.docx - full math, benchmarks, Lean 4 proofs.

## Slide 12
Why this matters (the 20-second version)
Every trainable decision lives in a convex equation with a unique global optimum - the 'barren plateau' problem that stalls quantum machine learning is structurally eliminated, not mitigated.
Benchmarks: 8.8x to 25.2x better than the strongest classical reservoir baseline on chaotic forecasting - and the online version even beats the batch one on Lorenz.
The learned parts are frozen; the human part takes two minutes; the dangerous part is hardware.
That is why this demo is safe enough to do in front of a live audience - and why the arm is waiting for you, Arinzay.
github.com/ElBalor/edge-of-chaos - The-Ghost-Lattice

## Slide 13
Connect the things.
Headband on. Two minutes. Send 'A'. The Ghost-Lattice is already dreaming - you just teach it your signature.
From the Grimoire of Elbàlor - The Digital Necromancer